## Slide 1
United States: FDA Pathway
European Union: MDR + AI Act
Clinical humanoid robot
novel device, no predicate
510(k) not viable, use De Novo
21 CFR 513(f)(2)
Pre-Submission meeting with FDA
risk class and evidence plan
De Novo request submission
bench, non-clinical, clinical evidence
FDA review, about 12 months
classification order issued
OUTCOME: Class II authorization
post-market surveillance
Clinical humanoid robot
novel device, no CE predicate
EU MDR Class IIb/III assessment
Notified Body required
EU AI Act: high-risk AI system
Art. 6, conformity Aug 2026
Clinical investigation (MDR Art. 62)
Competent Authority and ethics committee
CE marking by Notified Body
AI Act declaration of conformity
OUTCOME: EU market authorization
post-market clinical follow-up (PMCF)
Critical gap (both tracks)
No accepted safety standard for bipedal gait in patient-proximate environments. ISO 13482 excludes medical devices; ISO/TS 15066 covers only fixed-base collaborative arms.